## Slide 1: The Field of Catalysis – Today 1st January 2018 National Centre for Catalysis Research Indian Institute of Technology Madras

## Slide 2
Typical Unresolved issues in Catalysis so far:
Key unresolved issues include the epoxidation of ethene with silver as a catalyst. Different conflicting models exist on how the precise composition of the silver surface influences this reaction. This factor determines the selectivity of the catalyst and therefore also the optimization of the process. Another example is the hydrogenation of ethene on a metal surface. Again: what is the exact structure of the surface during the reaction? Is it the naked metal surface, or is the surface filled with organic intermediates? We also lack basic insight into the synthesis of zeolites for catalysts. What role does molecular recognition play in building intermediates at a molecular level, when producing a zeolite? Or is the building of the structure a collective process, in which molecules are reorganized in a gel, without molecular recognition on a piecemeal basis. In Fischer Tropsch catalysis, several groups have reported on particle size effects for cobalt. Other groups have denied these effects, stating “cobalt is cobalt is cobalt.” We are seeing the emergence of theory to understand the (non-)existence of this particle size effect .
Future perspective in catalysis a Dutch study Dutch National school combination

## Slide 6: Role of Catalysis in a National Economy
24% of GDP from Products made using catalysts (Food, Fuels, Clothes, Polymers, Drug, Agro-chemicals)
> 90 % of petro refining & petrochemicals processes use catalysts
90 % of processes & 60 % of products in the chemical industry
> 95% of pollution control technologies
Catalysis in the production/use of alternate fuels (NG,DME, H2, Fuel Cells, biofuels…)

## Slide 7: Why R&D in catalysis is important
For discovery/use of alternate sources of energy/fuels/raw material for chemical industry
For Pollution control
For preparation of new materials
(organic & inorganic-eg: Carbon Nanotubes)

## Slide 8
Three Scales of Knowledge Application

## Slide 9: Some Developments in Industrial catalysis-1 1900- 1920s
Industrial Process Catalyst
1900s: CO + 3H2  CH4 + H2O Ni
Vegetable Oil + H2  butter/margarine Ni
1910s: Coal Liquefaction Ni
N2 + 3H2  2NH3 Fe/K
NH3 NO NO2 HNO3 Pt
1920s: CO + 2H2  CH3OH (HP) (ZnCr)oxide
Fischer-Tropsch synthesis Co,Fe
SO2  SO3 H2SO4 V2O5

## Slide 10: Industrial catalysis-2 1930s and 1940s
1930s:Cat Cracking(fixed,Houdry) Mont.Clay
C2H4 C2H4O Ag
C6H6  Maleic anhydride V2O5
1940s:Cat Cracking(fluid) amorph. SiAl
alkylation (gasoline) HF/acid- clay
Platforming(gasoline) Pt/Al2O3
C6H6 C6H12 Ni

## Slide 11: Industrial catalysis-3 1950s
C2H4 Polyethylene(Z-N) Ti
C2H4 Polyethylene(Phillips) Cr-SiO2
Polyprop &Polybutadiene(Z-N) Ti
Steam reforming Ni-K- Al2O3
HDS, HDT of naphtha (Co-Mo)/Al2O3
C10H8  Phthalic anhydride (V,Mo)oxide
C6H6  C6H12 (Ni)
C6H11OH C6H10O (Cu)
C7H8+ H2 C6H6 +CH4 (Ni-SiAl)

## Slide 12
Butene Maleic anhydride (V,P) oxides
C3H6  acrylonitrile(ammox) (BiMo)oxides
Bimetallic reforming PtRe/Al2O3
Metathesis(2C3 C2+C4) (W,Mo,Re)oxides
Catalytic cracking Zeolites
C2H4 vinyl acetate Pd/Cu
C2H4  vinyl chloride CuCl2
O-Xylene Phthalic anhydride V2O5/TiO2
Hydrocracking Ni-W/Al2O3
CO+H2O H2+CO2 (HTS) Fe2O3/Cr2O3/MgO
--do-- (LTS) CuO-ZnO- Al2O3
Industrial catalysis-4 1960s

## Slide 13
Xylene Isom( for p-xylene) H-ZSM-5
Methanol (low press) Cu-Zn/Al2O3
Toluene to benzene and xylenes H-ZSM-5
Catalytic dewaxing H-ZSM-5
Autoexhaust catalyst Pt-Pd-Rh on oxide
Hydroisomerisation Pt-zeolite
SCR of NO(NH3) V/ Ti
MTBE acidic ion exchange resin
C7H8+C9H12 C6H6 +C8H10 Pt-Mordenite
Industrial catalysis-5 1970s

## Slide 14
Ethyl benzene H-ZSM-5
Methanol to gasoline H-ZSM-5
Vinyl acetate Pd
Improved Coal liq NiCo sulfides
Syngas to diesel Co
HDW of kerosene/diesel.GO/VGO Pt/Zeolite
MTBE cat dist ion exchange resin
Oxdn of methacrolein Mo-V-P
N-C6 to benzene Pt-zeolite
Industrial catalysis-6 1980s

## Slide 15
DMC from acetone Cu chloride
NH3 synthesis Ru/C
Phenol to HQ and catechol TS-1
Isom of butene-1(MTBE) H-Ferrierite
Ammoximation of cyclohexanone TS-1
Isom of oxime to caprolactam TS-1
Ultra deep HDS Co-Mo-Al
Olefin polym Supp. metallocene cats
Ethane to acetic acid Multi component oxide
Fuel cell catalysts Rh, Pt, ceria-zirconia
Cr-free HT WGS catalysts Fe,Cu- based
Industrial catalysis-7 1990s

## Slide 16: Industrial catalysis-8 2000+
Solid catalysts for biodiesel
- solid acids, Hydroisom catalysts
Catalysts for carbon nanotubes
- Fe (Ni)-Mo-SiO2
For Developed Catalysts MAINLY IMPROVEMENT IN PERFORMANCE by New Synthesis Methods & use of PROMOTERS

## Slide 17: Green Chemistry is Catalysis
Pollution control (air and waste streams; stationary and mobile)
Clean oxidation/halogenation processes using O2,H2O2 (C2H4O, C3H6O)
Avoiding toxic chemicals in industry
(HF,COCl2 etc)
Fuel cells (H2 generation)
Latest Trends

## Slide 18: Catalysis in Nanotechnology
Methods of Catalyst preparation are most suited for the preparation of nanomaterials
Nano dimensions of catalysts
Common prep methods
Common Characterization tools
Catalysis in the preparation of carbon nanotubes
Latest Trends

## Slide 19: Catalysis in the Chemical Industry
Hydrogen Industry(coal,NH3,methanol, FT, hydrogenations/HDT,fuel cell)
Natural gas processing (SR,ATR,WGS,POX)
Petroleum refining (FCC, HDW,HDT,HCr,REF)
Petrochemicals (monomers,bulk chemicals)
Fine Chem. (pharma, agrochem, fragrance, textile,coating,surfactants,laundry etc)
Environmental Catalysis (autoexhaust, deNOx, DOC)
Latest Trends

## Slide 20: Big picture: Sustainable Development

## Slide 21: Green Chemistry Is About...
Cost
Waste
Materials
Hazard
Risk
Energy
Reducing

## Slide 22
The drivers of green chemistry
Green chemistry
Less
hazardous materials
High fines for waste
Producer
responsibility
Government legislation
Lower
capital investment
Lower
operating costs
Economic benefit
Pollution control
Safer
and smaller plants
Improved
public image
Societal pressure

## Slide 23: Green Catalytic Processes
Alternative feedstocks, reagents, solvents, products
Enhanced process control
New catalysts
Greater integration of catalysis and reactor engineering:
membrane reactors, microreactors, monolith technology, phenomena integration
Increased use of natural gas and biomass as feedstock
Photodecomposition of water into hydrogen and oxygen
Catalysts for depolymerizing polymers for recycle of the monomers
Improvements in fuel cell electrodes and their operation

## Slide 24: Cleaner and greener Environment: Catalysis
New directions for research driven by market, social & environmental needs:
Catalysis for energy-friendly technologies and processes (primary methods)
New advanced cleanup catalytic technologies (secondary methods)
Catalytic processes and technologies for reducing the environmental impact of chemical and agro-industrial solid or liquid waste and improving the quality and reuse of water (secondary methods)
Catalytic processes for a sustainable chemistry (green chemistry and engineering approach)
Replacement of environmentally hazardous catalysts in existing processes

## Slide 25: How to Decrease the Greenhouse Effect?
New catalysts for high output fuel cells
Electricity production via electrocatalytic oxidation of hydrocarbons
Chemical energy of hydrocarbon is converted to electricity
Catalysts and processes for solar energy conversion and hydrogen
production
CO2 or other greenhouse gases are not emitted into the atmosphere,
First solar energy is converted into the chemical energy of synthesis gas (CO + H2) via the endothermic reaction of methane reforming
Storage of the synthesis gas
The stored energy can be released via the reverse exothermal methanation reaction
CO + 3H2 → CH4 + H2O
Efficiency from 43 to 70 %
Catalysts are needed for these reactions!!!

## Slide 26
Examples of Green Catalysis

## Slide 27
Examples of Green Catalysis

## Slide 28: “The use of auxiliary substances (e.g. solvents, separation agents, etc.) should be minimized”
Examples of Green Catalysis

## Slide 29: Poly lactic acid (PLA) for plastics production
Examples of Green Catalysis

## Slide 30: Polyhydroxyalkanoates (PHA’s)
Examples of Green Catalysis

## Slide 31: Photocatalysis
Photocatalyst
Starch + O2
Organic compound
Chlorophyll
CO2
H2O
CO2 + H2O
Organic
Compound
+ H2O + O2

## Slide 32: Photocatalytic Applications

## Slide 33: TiO2 - Photocatalysis
3.12 eV (380 nm)

## Slide 34
Some Potential Problems
Short residence times require fast reactions
Fast reactions require very active catalysts that are stable (The two most often do not go together)
Catalyst deactivation and frequent reactor repacking or reactivation
Fouling and clogging of channels
Leaks between channels
Malfunctioning of distributors
Reliability for long time on-stream
Structural issues
So far there are only two major commercial uses of micro-channel systems (monoliths) –
Automotive catalytic convectors (major success)
Selective catalytic reduction (NH3 – SCR) of power plant NOx
Notes: S18 The following question then arises. With all their perceived advantages, and the technologies available to manufacture micro reactors in silicon, in glass and in steel, or other metals, why aren’t they more widely used?
The answer is that they require very fast reactions and active stable catalyst (usually these two do not go together).
Most importantly micro reactors are, due to small dimensions, more prone to fouling and clogging, leaks between channels, and their reliability and life on stream is an unknown.
All of these are potentially solvable problems on a case by case basis. However, the perceived risk factor is too large for them to replace existing installations.
Most likely acceptance of micro-devices will occur in the consumer products, distributed power systems, highly energetic fast reactions, in-situ production of hazardous chemicals. Other applications will be slower.

## Slide 35: Applications of the Process Utilizing Biomass Streams
Biomass
Waste
Aqueous
Biomass
Stream
Extraction
Extraction
PEM
Fuel Cell
SOFC
ICE
Genset
Microturbine
Genset
Hydrogen
APR
Fuel Gas
APR
Energy
Crops
Process
Hydrogen

## Slide 36: Biomass Sources For Biofuels
LignoCellulose (Cellulose, Hemicellulose, Lignin)
Starch
Sugars
Lipid Glycerides (Vegetable Oils & Animal Fats)

## Slide 37: Pathways to Renewable Transportation Fuels
Biomass
Gasifier
Pyrolysis
Hydrolysis
Syngas
Bio Oils
Methanol,
Ethanol,
FT( diesel,etc)
Refine to Liquid
Fuels
Ferment to
ethanol,
butanol
Aqueous phase
Reforming
Hydrogen
Gasoline
additives
Veg Oils
Algae Oils
Biodiesel

## Slide 38: Bioethanol Overview - Global
Current bioethanol production in US is 12 billion gallons.
Most cars on the road in US today can run on blends of up to 10% ethanol.
US DOE has estimated that there is a potential to produce over 80 Billion gallons of bio-ethanol from cellulose and hemi-cellulose present in corn biomass in the 9 major US corn producing states.
This equates to over 250 Million tons of bio-ethanol and >$160 Billion revenue.
Iogen’s Demo plant producing cellulosic ethanol from wheat straw in Canada since 2004.
DuPont-Danisco JV has started demonstration of cellulosic ethanol from corncobs since Jan., 2010 in USA.
Brazil currently blends 25% ethanol in gasoline and bioethanol is produced directly from sugarcane.
Brazilian flex cars are capable of running on just hydrated ethanol (E100), or just on a blend of gasoline with 20 to 25% anhydrous ethanol, or on any arbitrary combination of both fuels
China uses 10% bioethanol in gasoline .

## Slide 40: Natural gas to Transportation Fuels : Options
Natural Gas  Syngas
I. Syngas Methanol (DME)  Gasoline
II. Syngas  Fischer-Tropsch Syndiesel
Syndiesel Can use existing infrastructure
III. Syngas  H2  Fuel Cell – driven cars: Stationary vs On-board supply options for Hydrogen
Natural Gas Electricity;MCFC and SOFC can generate electricity by direct internal reforming of NG at 650C;Ni/ Zr(La)Al2O4, loaded on anode

## Slide 41: Catalysts for conversion of NG to Transportation Fuels
I.Syngas Preparation
Hydrodesulphurisation(Co/Ni-Mo-alumina)
Syngas generation(H2/ CO); POX, steam, autothermal, “dry” reforming; Ni(SR),Ru(POX) – based catalysts; Pt metals for POX for FT.
2.Fischer Tropsch Synthesis:
Co – Wax and mid dist; Fe - gasoline; Cu & K added.
Supported Co preferred due to its lower WGS activity & consequent lower loss of C as CO2.
3.Product Work up:
Wax Conversion to diesel and gasoline.
Mild Hydro-cracking/Isom catalysts
(Pt metal- acidic oxide support )

## Slide 42: Petroleum - vs- Syngas :: Diesel
Property Petro- Syn-
Boiling Range,oC 150-300 150-300
Density at 15 C,kg/m3 820-845 780
S, ppm vol 10 - 50 <1
Aromatics,% vol 30 <0.1
Cetane No >51 >70
CFPP, oC -15 -20
Cloud point,oC -8(winter) -15
Due to lower S, N and aromatics, GTL diesel generates less SOx and particulate matter.

## Slide 43: Power and fuels from Coal / PetCoke Gasification Texaco EECP Project
FEED:1235 TPD OF PetCoke
PC  SG  (75%)Power Plant
 25%FT fuel(tail gas Power)
55 MW Electricity; Steam.
20 tpd diesel; 4 tpd naptha
82 tpd Wax(60 tpd diesel); 89 tpd S;
H2: CO = 0.67;Once-thru slurry(Fe) FT reactor; RR = 15 % at a refinery site.

## Slide 44: Coal To Syngas To Fuel Cells
Catalysis in Coal / PetCoke gasification
SR: C + H2O CO + H2 (+117 kJ/mol)
Combust:2C+ O2  2CO (H = -243 kJ/mol)
WGS :CO + H2O  H2 + CO2 ( -42 kJ/mol)
Methan: CO+3 H2  CH4 + H2O(- 205 kJ/mol)
Methanation can supply the heat for steam gasification and lower oxygen plant cost. K & Fe oxides lower temp of gasification
H2/CO ~0.6 in coal gasification;Good WGS is needed;
MCFC and SOFC can use H2,CO, & CH4 as
fuel to generate electricity.
Low rank coals, Lignites gasify easier.

## Slide 45: Hydrogen Production Costs (The Economist / IEA)
SOURCE USD / GJ
Coal / gas/ oil/ biodiesel 1-5
NG + CO2 sequestration 8-10
Coal + CO2 sequestration 10-13
Biomass(SynGas route) 12-18
Nuclear (Electrolysis) 15-20
Wind (Electrolysis) 15-30
Solar (Electrolysis) 25-50

## Slide 47: Catalysts for H2O and CO2 Photothermal Splitting Using Sunlight
1. H2O  H2 + 0.5 O2
2. CO2  CO +0.5 O2
FT Synthsis: CO + H2 (CH2)n petrol/Diesel
Sandia’s Sunlight To Petrol Project: Cobalt ferrite loses O atom at 1400o C; When cooled to 1100o C in presence of CO2 or H2O, it picks up O, catalyzing reactions 1 and 2; Solar absorber provides the energy.
Challenge: Find a solid which loses / absorbs O from H2O / CO2 reversibly at a lower temp.

## Slide 48: Splitting H2O

## Slide 49: Future Fuels: Catalysis Challenges
Meeting Specifications of Future Fuels
Remove S,N, aromatics, Particulate Matter
Power Generation
- Lower CO2 Production in Catalytic Gasification
- Lower CO2 and H2/CO ratio in Syngas generation
FT Synthesis: Lower CH4 and CO2 ;Inhibit metal sintering; Increase attrition strength; Reactor design
Biomass:1.Cellulose to Ethanol ( enzymes)
2. Biomass gasification catalysts.
Decentralized Production/ Use of H2 and Biofuels will avoid costs due to their storage and distribution.
“Holy Grail “ Challenges
Direct Conversion of CH4 to methanol and C5+.
Catalytic Water and CO2 splitting using solar energy

## Slide 50
Future Challenges in Heterogeneous Catalysis: Understanding Catalysts under Dynamic Reaction Conditions
Dr. Kai F. Kalz, Dr.‐Ing. Ralph Kraehnert, Dr. Muslim Dvoyashkin, Prof. Dr.‐Ing. Roland Dittmeyer, Prof. Dr. Roger Gläser, Prof. Dr.‐Ing. Ulrike Krewer, Prof. Dr. Karsten Reuter and Prof. Dr. Jan‐Dierk Grunwaldt ChemCatChem. 2017 Jan 9; 9(1): 17–29.
In the future, (electro‐)chemical catalysts will have to be more tolerant towards a varying supply of energy and raw materials. This is mainly due to the fluctuating nature of renewable energies. For example, power‐to‐chemical processes require a shift from steady‐state operation towards operation under dynamic reaction conditions. This brings along a number of demands for the design of both catalysts and reactors, because it is well‐known that the structure of catalysts is very dynamic. However, in‐depth studies of catalysts and catalytic reactors under such transient conditions have only started recently. This requires studies and advances in the fields of 1) operando spectroscopy including time‐resolved methods, 2) theory with predictive quality, 3) kinetic modelling, 4) design of catalysts by appropriate preparation concepts, and 5) novel/modular reactor designs. An intensive exchange between these scientific disciplines will enable a substantial gain of fundamental knowledge which is urgently required. This concept article highlights recent developments, challenges, and future directions for understanding catalysts under dynamic reaction conditions.

## Slide 51
For understanding catalysts under dynamic reaction conditions different scientific disciplines such as (operando) spectroscopy, theory and kinetic modelling have to work hand in hand in order to provide a basic understanding of the relevant processes at the catalyst surface and the bulk. In a second step, this knowledge can then be implemented into the design of novel materials and reactor concepts. Fluctuations of the incoming variables concentration (c), pressure (p), temperature (T) and eventually electric potential (E) influence the local state of the catalyst and thereby lead to variations of the product stream composition in the form of concentration (c), conversion (X), yield (Y) and selectivity (S) of a specific product.

## Slide 53
  New and Future Developments in Catalysis
  Chapter 1 - Metal Catalysts for the Conversion of Biomass to Chemicals, Pierre Gallezot
  Chapter 2 - Current Catalytic Processes for Biomass Conversion, Hirokazu Kobayashi, Atsushi Fukuoka
  Chapter 3 - Emerging Catalysis for 5-HMF Formation from Cellulosic Carbohydrates, Z. Conrad Zhang
  Chapter 4 - Trends and Challenges in Catalytic Biomass Conversion, Christian Mårup Osmundsen, Kresten Egeblad, Esben Taarning
  Chapter 5 - Catalytic Processes of Lignocellulosic Feedstock Conversion for Production of Furfural, Levulinic Acid, and Formic Acid-Based Fuel Components, B. Kamm, M. Gerhardt, G. Dautzenberg
  Chapter 6 - Synthetic Biology for Biomass Conversion, Christopher E. French, Damian K. Barnard, Eugene Fletcher, Steven D. Kane, Sahreena Saleem Lakhundi, Chao-Kuo Liu, Alistair Elfick
  Chapter 7 - Hybrid Plant Systems for Breeding and Gene Confinement in Bioenergy Crops, Albert P. Kausch, Adam Deresienski, Joel Hague, Michael Tilelli, Stephen L. Dellaporta, Kimberly Nelson, Yi Li
  Chapter 8 - An Introduction to Pyrolysis and Catalytic Pyrolysis: Versatile Techniques for Biomass Conversion
  Li Li, Jack S. Rowbotham, H. Christopher Greenwell, Philip W. Dyer
  9. Chapter 9 - Using Microwave Radiation and SrO as a Catalyst for the Complete Conversion of Oils, Cooked Oils, and Microalgae to Biodiesel, Miri Koberg, Aharon Gedanken
  10.Chapter 10 - Environmental Benefits of Integrated Algal Biorefineries for Large-Scale Biomass Conversion
  Bobban Subhadra
  11. Chapter 11 - Heterogeneous Catalysts for Biomass Conversion, Lei Jin, Chung-hao Kuo, Steven L. Suib
  12. Chapter 12 - Processing Issues in Biofuels Production , Richard S. Parnas, Michael Pomykala, Iman Noshadi
  13. Chapter 13 - Economic Analysis of Bioenergy: An Integrated Multidisciplinary Approach
  Fred V. Carstensen, Marcello Graziano, Natalia Vorotytseva, William E. Waite, Kathryn E. Parr
  14. Chapter 14 - Biofuels of the Present and the Future, Arnold L. Demain, Marco A. Báez-Vásquez
  15.Chapter 15 - Catalysts for Biomass Conversion

## Slide 54
  New and Future Developments in Catalysis
  Introduction
  Chapter 1 - Metal Catalysts for the Conversion of Biomass to Chemicals, Pierre Gallezot
  Chapter 2 - Current Catalytic Processes for Biomass Conversion, Hirokazu Kobayashi, Atsushi Fukuoka
  Chapter 3 - Emerging Catalysis for 5-HMF Formation from Cellulosic Carbohydrates , Z. Conrad Zhang
  Chapter 4 - Trends and Challenges in Catalytic Biomass Conversion, Christian Mårup Osmundsen, Kresten Egeblad, Esben Taarning
  Chapter 5 - Catalytic Processes of Lignocellulosic Feedstock Conversion for Production of Furfural, Levulinic Acid, and Formic Acid-Based Fuel Components, B. Kamm, M. Gerhardt, G. Dautzenberg
  Chapter 6 - Synthetic Biology for Biomass Conversion, Christopher E. French, Damian K. Barnard, Eugene Fletcher, Steven D. Kane, Sahreena Saleem Lakhundi, Chao-Kuo Liu, Alistair Elfick
  Chapter 7 - Hybrid Plant Systems for Breeding and Gene Confinement in Bioenergy Crops, Albert P. Kausch, Adam Deresienski, Joel Hague, Michael Tilelli, Stephen L. Dellaporta, Kimberly Nelson, Yi Li
  Chapter 8 - An Introduction to Pyrolysis and Catalytic Pyrolysis: Versatile Techniques for Biomass Conversion, Li Li, Jack S. Rowbotham, H. Christopher Greenwell, Philip W. Dyer
  Chapter 9 - Using Microwave Radiation and SrO as a Catalyst for the Complete Conversion of Oils, Cooked Oils, and Microalgae to Biodiesel, , Pages 209-227, Miri Koberg, Aharon Gedanken
  Chapter 10 - Environmental Benefits of Integrated Algal Biorefineries for Large-Scale Biomass Conversion,, Bobban Subhadra
  Chapter 11 - Heterogeneous Catalysts for Biomass Conversion, Lei Jin, Chung-hao Kuo, Steven L. Suib
  Chapter 12 - Processing Issues in Biofuels Production, Richard S. Parnas, Michael Pomykala, Iman Noshadi
  Chapter 13 - Economic Analysis of Bioenergy: An Integrated Multidisciplinary Approach, , Fred V. Carstensen, Marcello Graziano, Natalia Vorotytseva, William E. Waite, Kathryn E. Parr
  Chapter 14 - Biofuels of the Present and the Future, Arnold L. Demain, Marco A. Báez-Vásquez
  Chapter 15 - Catalysts for Biomass Conversion

## Slide 57
The chilean embargo on nitrates ( an ingredient for explosives in the early 1900s) to Germany boosted Haber and Bosch studies on the fixation of nitrogen in air to produce ammonia (1910-1916).
The need for more efficient automobile fuel that incited E.Houdry to research and develop the oil cracking process (ca1935).
Catalytic reforming and hydrocarbon alkylation developed by UOP in the later 30s and early 40s not only providing higher octane index fuels but also enabling, because of their availability, the British RAF pilots to win the Battle of Britain in the summer of 1940.
Environmental regulations that triggered the development of various catalytic hydrotreating processes, the three way exhaust catalyst, the MTBE and TAME synthesis process and various technologies to reduce NOx Emission.

## Slide 58
Todays major pullers are:
Market driven strategy aiming at simpler and less capital intensive processes and the access to abundant, renewable and cheaper feeds;
Societal concern for preservation and remediation of the environment;
Evolving legislations by public/governmental bodies: often fluctuating with time because of the various bodies and lobbies are involved, but eventually always having strict deadlines;
Weak signals from world-wide scientific progress(academic and industrial) because of industry’s awareness of developments made by competitors and fortunately also the identification of creative projects, advances and discoveries in academia.

## Slide 62
Schematic future scenario for power‐to‐chemicals processes demonstrating the importance of the development of more tolerant catalysts and processes a) time‐dependent power production by wind energy in 48 h (source: Fraunhofer ISE, KW 9, 2015), b) smoothed profile of hydrogen by intermediate storage

## Slide 63
Typical time and length scales relevant for dynamic processes in catalysis. Blue: molecular processes at the active site; green: processes involving solid state catalysts, yellow: transport processes of reactants and products. The time frame important for dynamic operation addressed in the present concept article (indicated with a red box) includes microscopic and macroscopic length scales.

## Slide 71: 2001 -2005 AD 1. Zeolites as catalysts for fine chemicals and pharmaceuticals synthesis 2. Use of solid acid catalysts in fine chemicals synthesis 3. Biocatalytic removal of S,N, and metals from petroleum feedstocks 4.Extensive use of metallocenes and other single site catalysts for polymer synthesis 5.Alkene to alkane feedstock transition 6.Catalytic combustion to decrease VOCs and Nox emissions

## Slide 72: 2005-2010 AD 1.Nanotechnology in catalyst manufacture 2. Chemical and biochemical (bifunctional, Cascade) catalysts 3. Engineered enzymes in chemicals/fuel production 4.chiral polymeric materials 5. Heterogeneous catalysts for assymmetric synthesis of fine chemicals

## Slide 73: 2010-2020 AD 1. Fuel cell powered vehicles 2. High temperature inorganic-organic polymers 3. membranes and other multi-functional catalysts 4. Broader use of electro- and photo-catalysis 5. Advent of biopolymers 6. Bio-gradable materials and bio-silk

## Slide 74: 2020 -2040 AD 1. Photolytic water splitting and Hydrogen economy 2. Catalytic antibodies – biomimetics and synthetic enzymes in fine chemical and pharmaceutical synthesis 3. Engineering microbes/bacteria for fine chemical synthesis 4. Production of chemicals in living plants

## Slide 78
Metal Oxides in Heterogeneous Catalysis is an overview of the past, present and future of heterogeneous catalysis using metal oxides catalysts. The book presents the historical, theoretical, and practical aspects of metal oxide-based heterogeneous catalysis. Metal Oxides in Heterogeneous Catalysis deals with fundamental information on heterogeneous catalysis, including reaction mechanisms and kinetics approaches. There is also a focus on the classification of metal oxides used as catalysts, preparation methods and touches on zeolites, mesoporous materials and Metal-organic frameworks (MOFs) in catalysis. It will touch on acid or base-type reactions, selective (partial) and total oxidation reactions, and enzymatic type reactions The book also touches heavily on the biomass applications of metal oxide catalysts and environmentally related/depollution reactions such as COVs elimination, DeNOx, and DeSOx. Finally, the book also deals with future trends and prospects in metal oxide-based heterogeneous catalysis. In Metal Oxides in Heterogeneous Catalysis, by Jacques C Vedrine

## Slide 79: Role of Catalysis in a National Economy
24% of GDP from Products made using catalysts (Food, Fuels, Clothes, Polymers, Drug, Agro-chemicals)
> 90 % of petro refining & petrochemicals processes use catalysts
90 % of processes & 60 % of products in the chemical industry
> 95% of pollution control technologies
Catalysis in the production/use of alternate fuels (NG,DME, H2, Fuel Cells, biofuels…)

## Slide 80: Green Catalytic Processes
Alternative feedstocks, reagents, solvents, products
Enhanced process control
New catalysts
Greater integration of catalysis and reactor engineering:
membrane reactors, microreactors, monolith technology, phenomena integration
Increased use of natural gas and biomass as feedstock
Photodecomposition of water into hydrogen and oxygen
Catalysts for depolymerizing polymers for recycle of the monomers
Improvements in fuel cell electrodes and their operation

## Slide 81: Cleaner and greener Environment: Catalysis
New directions for research driven by market, social & environmental needs:
Catalysis for energy-friendly technologies and processes (primary methods)
New advanced cleanup catalytic technologies (secondary methods)
Catalytic processes and technologies for reducing the environmental impact of chemical and agro-industrial solid or liquid waste and improving the quality and reuse of water (secondary methods)
Catalytic processes for a sustainable chemistry (green chemistry and engineering approach)
Replacement of environmentally hazardous catalysts in existing processes

## Slide 82: How to Decrease the Greenhouse Effect?
New catalysts for high output fuel cells
Electricity production via electrocatalytic oxidation of hydrocarbons
Chemical energy of hydrocarbon is converted to electricity
Catalysts and processes for solar energy conversion and hydrogen
production
CO2 or other greenhouse gases are not emitted into the atmosphere,
First solar energy is converted into the chemical energy of synthesis gas (CO + H2) via the endothermic reaction of methane reforming
Storage of the synthesis gas
The stored energy can be released via the reverse exothermal methanation reaction
CO + 3H2 → CH4 + H2O
Efficiency from 43 to 70 %
Catalysts are needed for these reactions!!!

## Slide 83: Future Fuels: Catalysis Challenges
Meeting Specifications of Future Fuels
Remove S,N, aromatics, Particulate Matter
Power Generation
- Lower CO2 Production in Catalytic Gasification
- Lower CO2 and H2/CO ratio in Syngas generation
FT Synthesis: Lower CH4 and CO2 ;Inhibit metal sintering; Increase attrition strength; Reactor design
Biomass:1.Cellulose to Ethanol ( enzymes)
2. Biomass gasification catalysts.
Decentralized Production/ Use of H2 and Biofuels will avoid costs due to their storage and distribution.
“Holy Grail “ Challenges
Direct Conversion of CH4 to methanol and C5+.
Catalytic Water and CO2 splitting using solar energy

## Slide 84
Theory and Computation for Catalysis
Scientific Challenges and Research Approaches Defining molecular models of reactants and catalysts . Accurate prediction of potential energy surfaces . Characterizing potential energy surfaces—understanding the structures of working catalysts Accurate prediction of entropies and free energies. Accurate prediction of reaction rate constants .
Coupling the dynamics of electrons and nuclei. Spanning temporal and spatial scales—multiscale methods . High-performance computing—harnessing the power of peta-scale and exa-scale computational resources for computational catalysis . Design and controlled synthesis of catalytic structures—a new challenge for theory and computation

## Slide 85: The story goes on ……….century after century Thank you all